## Slide 1: Lab 4 overview + tips
- Aalhad Patankar, Bryan Li, David Watkins

## Slide 2: Lab overview
Goals:
Follow a yellow line using computer vision
Correct yourself when veering off course
U-turn when orange stop line is encountered (at a certain distance)
Extra credit: Achieve a turn

## Slide 3: One possible architecture
Find position
Capture Image
Apply Homography
Filter colors
Find hough lines
Determine angle/distance
Stop sign
Detect Stop Sign
Controller
Move robot to center line
Move forward
U-turn

## Slide 4: Additional helpful modules
GPG2 control module wrapper to easily move and turn robot
Camera module to control camera settings/config
Homography module or script to obtain the correct transform and session parameters you will need
Testing module to automatically iterate through testbed
Try not to write it all in one long script -- think about good coding practices

## Slide 5: Tips and hints
Purchase tape that we linked to in lab spec to be able to test anywhere on the go
  Or use the image set we gave you to do the same
Separate assignment into logical modules, and work in parallel to build + test modules. Mock up where appropriate
  E.g. To test position + pose estimation code, mock up valid hough line + robot position
Assign team roles. There are several components to this lab
  The core algorithms, software design + testing, integration, testing, etc.
Start early!!!

## Slide 6: Tips and hints
Develop good debugging tools early, will help you in the long run
Save good images so you can use them as mock data for modules
  raspistill command
Be careful when working in homography transformed space to make sure all the data points you're working with have also been transformed (if doing pose or position estimation)
Post on Piazza and help out teammates
This will be updated as new hints come up