## Slide 1: Learning Agile and Dynamic Motor Skills for Legged Robots
Jemin Hwangbo, Joonho Lee, Alexey Dosovitskiy, Dario Bellicoso, Joonho Lee, Vassilios Tsounis, Vladlen Koltun, and Marco Hutter
Presented by Steven Mazzola
UNI: slm2242

## Slide 2: Why Legged Robots?
Good alternative to wheeled robots for rough terrain or otherwise complicated environments
Can perform similar actions to humans or other animals
Leg length increases obstacle avoidance and climbing ability

## Slide 3
Boston Dynamics PETMAN
(hydraulic actuator)
Boston Dynamics BigDog (hydraulic actuator)
MIT Cheetah
(electric actuator)
Boston Dynamics SpotMini
(electric actuator)

## Slide 4: What's wrong with current systems?
Hydraulic actuator robots (PETMAN, BigDog)
  Advantage: uses conventional fuel, high energy output for size
  Disadvantages:
    Noisy and produces smoke. Cannot be used indoors without special accomodations
    Heavy and large. Limits robot to large size
Electric actuator robots (Cheetah, SpotMini)
  Cheetah: optimized mostly for speed, lacks general application capabilities
  SpotMini: inner working are kept secret

## Slide 5
ANYmal Robot
Bio-inspired dog-sized quadruped
Weight: 32 kg
4 legs, 55cm long, 3 degrees of freedom
  High leg-length to footprint ratio
12 Series-Elastic Actuators (SEAs)
  Electric motor
  High gear ratio transmission
  Elastic element
  Rotary encoders
    Spring deflection
    Output position

## Slide 6: Methodology

## Slide 7
1. Modeling
ANYbot is composed of rigid links and ball bearings at the joints.
Would a fully ideal model representation be sufficient?
What aspects would be difficult to model?
  Inertial properties
  Actuator dynamics

## Slide 8
1. Modeling

## Slide 9
2. Training
Actuators have non-linear dynamics and complex internal states
Self-supervised learning can be used to determine the action-to-torque relationship through an actuator network
Network uses history of position errors and velocity
  Current state and past two states at 0.01s interval
  Interval is sparse to prevent overfitting but dense enough to capture high frequency dynamics
  Tuned with validation error
Trained by generating foot trajectories, computing expected joint positions with inverse kinematics, and collecting error between predicted and real data.

## Slide 10: 2. Training
Multi-layer perception (MLP) actuator network
3 hidden layers of 32 units each
Softsign activation function

## Slide 11
3. Learning
Observation o(t): state measurement of robot
Action a(t): position command to actuator
Reward r(t): factor to promote desired behavior
Includes nine measurements: base orientation, base height, linear velocity, angular velocity, joint position, joint velocity, joint state history, previous action, command
Locomotor training uses all nine, while recovery training omits base height
Selected according to stochastic policy
Uses a fixed PD controller
  Kp set at value which keeps relative ranges of position and torque similar
  Kd set at high value to reduce oscillation

## Slide 12: 3. Learning
Multi-layer perception (MLP) actuator network
2 hidden layers of 256 and 128 units
Tanh activation function
Trust Region Policy Optimization (TRPO)
Custom implementation allows for 250,000 state transitions in 4 hours
Stop if no performance improvement in 300 iterations

## Slide 13
3. Learning
Need to find a balance for joint torque and velocity penalties
  Low penalty: unnatural motions
  High penalty: standing bias, limited movement
Curriculum:
  Learn primary objective first, then refine movement for other criteria
  Curriculum factor in range [0,1] added to all non-primary terms
    For locomotion, base velocity error cost is unaffected
    For recovery, base orientation cost is unaffected

## Slide 14
Locomotion
Recovery

## Slide 15
3. Learning
High-speed locomotion training:
  Send randomly sampled forward, lateral, and turning velocities as commands
  Trajectory executed for 6 seconds
  Simulation terminated if in violation of ground or other limits
  Training time: 4 hours
Recovery training:
  Robot collision bodies are given random sizes and positions
  Dropped from 1 meter in random configurations
  Simulation runs for 1.2 seconds and result is set as initial position for learning
  Training time: 11 hours

## Slide 16
4. Deployment
Trained parameters set by simulation are now ported to onboard PC
Position commands converted to torque commands to control real robot
Complexity of actuators complicate this transfer

## Slide 17: Video
https://www.youtube.com/watch?v=aTDkYFZFWug&feature=youtu.be

## Slide 18: Results
Locomotion policy:
A: Discovered gait for 1.0m/s forward velocity
B: Comparison of base velocity tracking accuracy for different gaits
C,D,E:
Comparison between controllers for different gaits

## Slide 19: Results
High speed policy:
A: Forward velocity
B: Joint velocities
C: Joint torques
D: Gait pattern

## Slide 20: Results
Actuation validation:
A: Validation set
B,C: 0.75m/s forward velocity
D,E: 1.6m/s forward velocity

## Slide 21: So what was achieved?
ANYmal gained locomotion skills derived purely from a simulated training environment on an ordinary computer.
Locomotion tests outperformed previous speed record on the ANYmal by 25%
Recovery rate was 100% after tuning joint velocity constraints, even in complex initial configurations
The simulation and learning framework created in this research can be roughly applied to any rigid body system

## Slide 22: Additional References
ANYmal: https://www.anybotics.com/anymal-legged-robot/
BostonDynamics: https://www.bostondynamics.com
MIT: http://biomimetics.mit.edu/
Thank you!