## Slide 1: Robot Programming Through Augmented Trajectories in Augmented Reality
Camilo Perez Quintero, Sarah Li, Matthew KXJ Pan, Wesley P. Chan, H.F. Machiel Van der Loos and Elizabeth Croft
2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS)
James Gong
4/23/19
Notes: Introduce self

## Slide 2: Background
Next generation of industrial manufacturing will involve robots working in a complementary fashion alongside skilled human workers
Augmented reality: facilitate interaction by enhancing the physical world with virtual information
Enables new human-robot interaction (HRI) possibilities
Notes: Industrial robots need to be re-programmed for a new task

## Slide 3: Augmented Reality
Industrial applications
  Assembly
  Training
  Maintenance
  Repair
Mobile device and head-mounted AR
In these applications, the human still performs the work
Webel et al. 2013
Notes: Web-based application
Human still doing the work

## Slide 4: Augmented Reality as an HRI interface
AR
Shared space
Novel HRI interface
Notes: Interaction methods and interfaces for HRI
Human operators’ intentions and interprets the task descriptions into a sequence of robot motions complying with the robot capabilities and the working requirements
Overlapping space that can be perceived by both the human user and the robot system

## Slide 5: Fang et al. (2013)
AR enables user to interact with the spatial environment prior to actual task execution
Notes: Web-based application
Human still doing the work

## Slide 6: System
Microsoft Hololens
  First untethered mixed reality head-mounted display
Robot arm
  Barrett Whole-Arm Manipulator (WAM)
  7-DOF
MYO armband
  1-DOF control input to move end effector along path
Notes: Web-based application
Human still doing the work

## Slide 7: Trajectory planning
Traditional methods non-intuitive and visually non-collocated
Two trajectory planning modes:
Free space trajectories
  Pick and place task
  Cube and sphere mark two anchor points
  Path is automatically generated
Surface trajectories
  Way-points set by the user via points set on the intersection between the surface of the 3D mesh and a ray coming from the virtual cursor
  Path interpolated from way points
Path calculation based on B-splines
Free space trajectory
Surface trajectory

## Slide 8: Interaction
Utilizing Hololens SDK libraries
Speech commands to change state
Virtual cursor controlled by head pose
Pinch hand gesture
Editing virtual paths
“Set point”
“Lock path”
User speech input

## Slide 9: Preview and editing
Virtual preview of robot motion
Initial position = current joint state of the real robot
Path can by dynamically changed using pinch gesture
“Generate”
“Edit”
User speech input

## Slide 10: Execution
Real robot executes planned trajectory
Autonomously or semi-autonomously
  User can control progression of motion through MYO band 1-DOF interface
“Pause”
“Reset”
User speech input

## Slide 11: Video
https://youtu.be/amV6P72DwEQ

## Slide 12: Experiment
10 test users
AR robotic interface and kinesthetic interface
Surface contact task
  Erasing sinusoid and straight line on white board
Free space task
  Pick up a plush toy and place it in a box

## Slide 13: Results
Average task completion time taken was significantly less using the AR interface
Users placed more way-points using the AR robotic system
NASA Task Load Index
  Kinesthetic interface requires a lower mental load
  However kinesthetic interface requires significantly increased physical effort
  Trade-off between physical and mental workload
Notes: simply changing the orientation of their head
trade-off between physical and mental workload

## Slide 14: Case Study: Carbon-fiber-reinforcement-polymer Manufacturing
Reduce wrinkles during the pleating step of the carbon-fiber-reinforcement-polymer vacuum bagging process
Able to remove majority of wrinkles

## Slide 15: Conclusion
Novel AR robotic interface for trajectory interaction
Validated system compared to kinesthetic teaching
Future improvements
  More agile path specification methods, such as setting multiple waypoints at once
  Force visualization and control, instead of constant force applied in normal direction