## Slide 1: COMS 6731 Humanoid Robots
Instructor: Dr. Peter Allen
Date: Tuesday, February 26th, 2019
Name: LianFeng Li, UNI: LL3226

## Slide 2: paper choice – learning topic
Title: Pouring Skills with Planning and Learning Modeled from Human Demonstrations
Title: Learning Pouring Skills from Demonstration and Practice (Shorter Version)
Author: Akihiko Yamaguchi, Christopher G. Atkeson, Scott Niekum, and Tsukasa Ogasawara
Videos:
  http://youtu.be/cGci9FOl680
  http://youtu.be/GjwfbOur3CQ

## Slide 3: architecture
Deriving a model learning from human demonstrations (Model skills manually)
Storing situation description + the parameters for the situation
Selecting a skill for a new situation with estimated parameters
Correcting the skill by adjusting its parameters to the new situation through actual executions

## Slide 4: Human demonstration
Poured dried granular materials (peas, rice, BBs) instead of liquid to avoid damage
Pouring consists of several steps:
  Hand reaching to a source container
  Grasping it
  Moving the source container to a receiving container
  Actual pouring
  Moving the source container to a position
  Releasing it
  Moving the hand to a final position

## Slide 5: inverse kinematics
The source container during pouring
  The edge point takes a constant value
  Only the orientation changes to control the flow
  Moves mostly in a 2-dimensional plane
  Modeled by a 1-dimensional variable, θ
  θ = 0 at the initial pose, and θmax is upside down
When the robot is grasping a source container, the position of the edge point of the source is constant in the local frame of the gripper.
Controlling the edge point is achieved by a standard inverse kinematics solver.

## Slide 6: Human demonstration
Phase 1: rotating the source container quickly until flow is observed
Phase 2: after flow starts, it continues without much rotating, rotates slowly until reaching target
Phase 3: after reaching the target amount, the human moves the source container to the final pose
Amount Ratio of 0.5 is half of receiver height

## Slide 7: experiment Setup
PR2 Robot
  Two 7-degrees of freedom arms with grippers
RGB cameras
  Measure the amount of poured material
  Detect specific colors in areas
Receiver
  Transparent plastic container
  Back half is colored
ROS packages:
  Low-level control, collision detection, and inverse kinematics solver of the grippers

## Slide 8: experiment Setup

## Slide 9: Flow control - Pouring
Robot uses the left hand to decrease complexity
Using Inverse Kinematic solver for the wrist link
The same three phases, but different speed

## Slide 10: Flow control - Pouring
Human Robot

## Slide 11: Flow control - Shaking
When jammed, robot shakes
  Shaking vertically VS. shaking at an angle of 45º
  Shaking with an angle is faster and is in accord with human demonstration

## Slide 12: Flow control - Tapping
When pouring a small amount, robot taps the container
  Initial flow dominates the total amount
  Hard to achieve accurate pouring with respect to the total amount

## Slide 13: on-line parameter optimizations
Focus on the pouring speed optimization (maximize the pouring speed = a score function)
  Score can be obtained through actual execution using following parameters
Discrete parameter optimization
  Discrete parameter is selected from a set of options, e.g. skill selection - most suitable for the task
  Use Boltzmann selection (the softmax selection)
Continuous parameter optimization
  Continuous parameter is selected from a single or multi dimensional continuous space
  e.g. a shaking axis - Skill-related parameters
  Use the Covariance Matrix Adaptation Evolution Strategy (CMA-ES) by Hansen, an evolutionary algorithm that does not require the gradient of the score function

## Slide 14: Learning - skill selection
Shaking A: shaking vertically
Shaking B: shaking at 45º
Select an skill for container shape and material type
3 options were tried in 1st
Shaking A dominant in 2nd and 3rd
Shaking A got stuck in 4th
Shaking B was selected

## Slide 15: Learning - skill selection
Only pouring at the beginning
Shaking B and A alternate
Shaking B jamming in 5th and 6th
Shaking A was selected
Shaking A: shaking vertically
Shaking B: shaking at 45º
Select an skill for container shape and material type

## Slide 16: Learning – shaking axis
Adjust skill parameters
Pouring duration = Score
  Faster = Higher
Choose angle randomly
Converge
  ~45º = 0.785 rad
Noisy in score plot
  CMA-ES help

## Slide 17: Generalization Ability
Flow control for various situations
  Container shapes
  Material types
Unknown situation
  Utilizing learning methods

## Slide 18
Spreading
Complete pouring behavior

## Slide 19
Thanks Questions?