## Slide 1: SMASHER
Jian Liu
Chaoying Kang
Tong Zhang
Instructor: Prof. Edwards
Columbia University in the city of New York

## Slide 2: Overview
Block Diagram
interrupt

## Slide 3: Rotary Switch
Two rotary switch to control four board
FSM to detect the input from switch
Send one interrupt when switch happened
Send add/sub signal during Interrupt

## Slide 4: Audio Module
Storage of sounds
First attempt to store program in the SDRAM
 Store audio memory in SRAM
 Stored together as alt_u16 array with 30K bytes
Four kinds of sounds
Audio module send interrupt continuously
CPU send 64bytes data to buffer in audio module for every interrupt

## Slide 5: Audio Module
Parameter of sounds
Sampling Frequency : 11 KHz(44KHz originally)
Interrupt Frequency : 1.34 KHz
Actual Frequency : 43 KHz
Challenges in Audio
Hard to store
Interrupt Frequency Limitation
Actual Frequency : 43 KHz

## Slide 6: VGA Module
Storage of Colors
Storage data on on-chip memory
 Using 16 colors indexed image
Two kinds of image display
    Sprite
    Tile (for the bugs)
VGA module send interrupt to update the data
Serveral animination

## Slide 7: C control
Each brick is treated as eight parts with different reflection behavior
Cloud board has six parts with different reflection direction and speed
Ball is located by five spots
If ball out of visual area, life is decreased and ball is re-positioned.

## Slide 8: C control
If win or lose, it will print “WIN” or “LOSE” consist of bricks. The pattern will print one after another brick and flash multi-times.
If multi-hits happens in a short time. Collision may happens. In this case, stop the current sound immediately, and start the new one.

## Slide 9: Thank You! Q&A