## Slide 1
Xiang Zhou xz2266
Hao Zheng hz2256
Ran Zheng rz2228
Younggyun Cho yc2704
Touch Pong

## Slide 2
Achievement

## Slide 3
1. First part of design is the communication between touch panel and DE2 board
2. The second part is designing verilog code
3. The final part is designing the game logic and develop C code
Design

## Slide 4
Basic frame of the communication

## Slide 5
Schematic of the system

## Slide 6
Hardware

## Slide 7
Hardware
Loading background into the Flash
We use flash to store background. We can download the picture from flash to SDRAM.

## Slide 8
Hardware
Generate mif file
A memory Initialization File (.mif) is an ASCII text file (with the extension .mif) that specifies the initial content of a memory block (CAM, RAM, or ROM), that is, the initial values for each address. This file is used during Quartus project compilation and simulation.
The MIF file serves as an input file for memory initialization in the Quartus compiler and simulator. You can also use a Hexadecimal Intel-Format File (.hex) to provide memory initialization data.
Img=imread('PINGPONG.BMP');
BW = Img;
R=BW(:,:,1);

## Slide 9: Software
The first thing code should do is to get the coordinates of both the ball and the rackets. Already do the signal transformation in the Verilog part, we can just use the coordinates of x_ y_pingpong and ltm_y_x. But the format of these coordinates which is 20 bits long with the x and y combined together is different from the nomal coordinates.

## Slide 10: Software
We decide which one is for the left rackets, which one is for right by change rules that racket can't move until the ball and the touch point reach the corresponding side.
By setting the movement step and the direction of the ball, and then adding then to the previous position, we can get the instant position of the ball.

## Slide 11: Software
We need to transmit the controlled data from the nios system to the LCD_Timing_Controller:
IOWR_ALTERA_AVALON_PIO_DATA(PIO_LED_BASE, score);
IOWR_ALTERA_AVALON_PIO_DATA(PIO_PINGPONG_BASE, x_y_pingpong);
IOWR_ALTERA_AVALON_PIO_DATA(PIO_LEFT_BASE, left_y_x);
IOWR_ALTERA_AVALON_PIO_DATA(PIO_RIGHT_BASE, right_y_x);

## Slide 12: Responsibilities
Ran Zheng: drafted original proposal; researched guide book and helped with whole system construction.
Hao Zheng: developed all aspects of hardware (modified Verilog code); built NIOS system and set up interruption; contributed to presentation slides and final report.
Xiang Zhou: developed algorithm; wrote software for control of game. Write part of the final report. Helped set hardware.
Younggyun Cho: helped write game logic; researched and initially implemented displaying image using ROM; loaded background into the DE2 Flash; Detected and fixed bugs; contributed to final report.