## Slide 1
WormCraft
Tianyi Zhang tz2210
Ning Li nl2447
Yuxuan Zhang yz2580
Ziwei Zhang zz2282

## Slide 2: overview
Game design introduction
System Architecture
VGA display
Wii mote
Audio control
Software implementation
Lessons learned

## Slide 3: Game introduction
A combat PVP game with Wii mote control
Motivated by game logic of Warms and Minecraft pixel-style components.
Strategies
Turn-based game logic
One will be defeated when hp goes to zero
Three types of bombs with explosion
2D Minecraft world
Wii mote controls move and attack freely

## Slide 4
Software
ARM Core
Avalon Bus
FPGA
VGA
Display
ROM
Decoder
Audio
CODEC
Peripheral
driver
Wii mote
System Architecture

## Slide 5: VGA Display
Prepocess pictures to follow the design sizing and requirement.
Using MATLAB to Convert picture to mif file which can be directly utilized by FPGA
All sprites saved in on chip memory
Implement different decoders to decode data with control signal from software
(Directly code in VGA mode costs long time for design and debug )

## Slide 6: Level of Sprites
Background
Game figures
and bombs
Game figures
Time/life/strength
Game figures
Map components
Game figures
Game effects

## Slide 7: Control data
 | 15 | 14 | 13 | 12 | 11 |  | 10 |  | 9 | 8 | 7 | 6 | 5 |  | 4 | 3 |  | 2 | 1 |  | 0
Hex0 | Number of crater |  |  |  |  |  |  |  | Vertical coordinates of grenade |  |  |  |  |  |  |  |  |  |  |  | 
Hex1 | Explosion figure |  |  |  |  |  |  |  | Horizonal coordinates of grenade |  |  |  |  |  |  |  |  |  |  |  | 
Hex2 | face | fig1 pic show |  |  |  |  |  |  | Vertical coordinates of figure No.1 |  |  |  |  |  |  |  |  |  |  |  | 
Hex3 | Health show of figure1 |  |  |  |  |  |  |  | Horizonal coordinates of figure No.1 |  |  |  |  |  |  |  |  |  |  |  | 
Hex4 | face | fig2 pic show |  |  |  |  |  |  | Vertical coordinates of figure No.2 |  |  |  |  |  |  |  |  |  |  |  | 
Hex5 | Health show of figure2 |  |  |  |  |  |  |  | Horizonal coordinates of figure No.2 |  |  |  |  |  |  |  |  |  |  |  | 
Hex6 |  | Fig | En | up/ down |  | Horizontal coordinate of pointer |  |  |  |  |  |  |  | Vertical coordinate of pointer |  |  |  |  |  |  | 
Hex7 | K.O. | Time_Counter 30 sec |  |  |  |  |  |  | Strength of throwing bomb |  |  |  |  |  | sound |  |  |  |  |  | 

## Slide 8: Audio
We implement three types of sound effects via Analog Devices SSM2603 audio CODEC (Encoder/Decoder).
FPGA and Audio codec communicates using I2C protocol.
The sampling rate is 44.1 kHz. The device is controlled by a serial I2C bus interface, which
is connected to the FPGA.

## Slide 9: Wii mote
Connect wiimote to the board via bluetooth
Utilizing BlueZ protocol stack for communication between board and peripheral device
Use Wiimote driver “libwiimote” to translate the packet into the desired format, including the corresponding button key, acceleration and gravity sensor’s coordinate value.

## Slide 10
Kernel
Bluetooth dongle
WII
lusb
bluez
libwiimote
APP
Vga_led.ko
Avalon Bus

## Slide 11
Start
Initialization
Get Wiimote Information and Update the Player Position
Run out of Life?
Y
N
Win
Write message into FPGA and display the corresponding image
Reset Game?
Y
N
Software
Flow chart

## Slide 12: Soil and Crater
We use a 2D array map [480][640] to determine whether this location has Soil or not.
To create a crater, we set the map [][] around explosion location to ‘0’

## Slide 13: Element blocked
32 pixels
44 pixels
for(n=0;n<44;n++){
left_blocked += map[y+n][x-1];
right_blocked += map[y+n][x+32];
}
for (n=0; n< 32; n++){
up_blocked += map[y-1][x+n];
down_blocked += map[y+44][x+n];
}

## Slide 14: Lessons Learned
Use Quartus to implement hardware design and debug errors
Software, processor, hardware and other components work in the one embedded system
Corporation as a team